## Slide 1: Enable Blind LLMs with Vision
---My Summer Research Summary
王杰，04/06/2024
Github: Summer_Research_2023
Advisor: 向为教授 Prof. Wei Xiang
Mentor: 黄莹莹 Yingying Huang
Visionary Co-Driver: LLMs Enhance Driver Perception of Potential Risks with AR-HUD
Notes: 我们为什么做这个工作，我们做这个工作有什么价值，架构逻辑要更清楚

## Slide 2: Content
Project Intuition
Model Selection
System Design
User Study
Failure and Success
Research Reflection
Visionary Co-Driver: LLMs Enhance Driver Perception of Potential Risks with AR-HUD

## Slide 3: Intuition: Corner cases are countless, but LLM has logic
Road scene understanding is a relative complex and important topic in autonomous driving field.
Traditional approach like driving risk field or object detection is useful and practical, but they can’t cover all the possibilities in the real-world scenario (Too much annoying if-statements).
Solving it in a brand-new way is my intuitive study interest, because I saw the potential capability within LLM to be a co-pilot, helping drivers to recognize and avoid those potential risk.
Visionary Co-Driver

## Slide 4: However, there is a huge gap between logic and reality: modality difference
The ChatGPT can 'think 'through text conversation, but it doesn’t have internal capability of perception.
Therefore, we need to provide a tool for it to "read" the road (Road Scene Understanding).
“有啥子在我前头啊？看不着啊”
Visionary Co-Driver

## Slide 5: Our solution: combine SOTA models together, obtain on-road information
A vision2text cascaded connected model, helping the LLM to detect the road
Visionary Co-Driver

## Slide 6: What is the Vision Feature of a pedestrian?
Location: road or sidewalk? Left or right side?
Distance: near or far from us?
Speed: fast or slow?
Type: old or young?
Visionary Co-Driver

## Slide 7: Segmentation: Segment Anything(SAM)
- [2023SOTA]
- Transformer based unlabeled segmentation, SOTA zero-shot segmentation
Visionary Co-Driver

## Slide 8: Divide the sidewalk from road
After segment everything, it’s clear that all the sidewalks are shown in the image.
Visionary Co-Driver

## Slide 9: But segment everything is expensive!
How can we obtain the mask information easily from SAM?
Visionary Co-Driver

## Slide 10: Take a review on SAM:
- can generate pixel level binary mask of the image
- Can be prompted by both point and box, including positive and negative prompt
Visionary Co-Driver

## Slide 11: Object detection: Grounding DINO
- [2022SOTA]
- Transformer based knowledge distillation, SOTA zero-shot detection.
- can generate bbox of the detected object using monocular image
Visionary Co-Driver

## Slide 12
- Can be prompted based on nature language
- The gDINO can successfully recoginze the road & sidewalk using contrast prompting
- Pedestrian detection is separate, optimizing the accuracy
Object detection: Grounding DINO
Visionary Co-Driver

## Slide 13: Take a review on SAM:
Combining with Grounding DINO, then we realize a SOTA semantic segmentation model
Visionary Co-Driver

## Slide 14: Now, how can we know the distance from pedestrian to us?
In industry practice: Radar & Lidar Sensor!
But: we are poor, and we only have monocular video…
Visionary Co-Driver

## Slide 15: Depth estimation: Dense Prediction Transformer(DPT)
- [2021SOTA]
- Transformer based monocular depth estimation
- can generate image-size NumPy array indicating the depth value of each pixel
- Based on it, we obtained the estimated distance from dashcam to object
Output: [very close, close, medium, far, very far]
Visionary Co-Driver

## Slide 16: Depth estimation: Dense Prediction Transformer(DPT)
- [2021SOTA]
- Transformer based monocular depth estimation
- can generate image-size NumPy array indicating the depth value of each pixel
- Based on it, we obtained the estimated distance from dashcam to object
Output: [very close, close, medium, far, very far]
Visionary Co-Driver

## Slide 17: LLM: gpt3.5_turbo_16k
- long memory, can analyze the road scene with appropriate prompting
output can be seen here (0728 version):
Summer_Research_2023/Blind_LLM_Guide_Project/Chatbot/
There was no long-context or RAG for long video.
Visionary Co-Driver

## Slide 18: SYSTEM Design
So, how do we connect those modal together into a pipeline?
Visionary Co-Driver

## Slide 19: Multiple Object Tracking Yolov8+ByteTrack
[2023 SOTA]
Official Support of the classic and powerful real-time CV: You Only Look Once
Fastest with GPU acceleration
Visionary Co-Driver

## Slide 20: How to use LLM locate potential risk? --- Output format
According to early test on LLM’s capability, it can evaluate the danger level and potential risk within the current driving scenario:
Pixel level classification, divide into 6 aspects
Visionary Co-Driver

## Slide 21: How to use LLM locate potential risk? --- Output format
Furthermore, how can we demonstrate it in: - Vision: ARHUD
- Unity enhanced Video
Our solution: 关键帧+混合帧分析
Visionary Co-Driver
Notes: 输出要说清楚，怎么交代给

## Slide 22: Vision2text
Text generation process
Visionary Co-Driver

## Slide 23: ARHUD
Augmented Reality Heads-Up Display (AR-HUD) interfaces
Visionary Co-Driver

## Slide 24: ARHUD
Augmented Reality Heads-Up Display (AR-HUD) interfaces
Visionary Co-Driver

## Slide 25: ARHUD
Augmented Reality Heads-Up Display (AR-HUD) interfaces
Visionary Co-Driver

## Slide 26: Another basic problem: how to test the model?
It occupies a lot of time to do simulation and real-life testing So, we choose video, - monocular - ground truth justification - many pedestrian
Visionary Co-Driver

## Slide 27: JAAD dataset --- the video dataset for pedestrian intention prediction
What is JAAD? Joint Attention in Autonomous Driving (JAAD) Dataset.
Purpose: Developed to study pedestrian behavior, interactions, and visual cues in the context of autonomous driving.
Content:
Videos: Over 240 high-resolution video clips from different urban locations.
Annotations: Includes detailed annotations for pedestrians, such as age, gender, actions, and signals.
Scene Information: Traffic conditions, weather, lighting, etc.
Attention and Intention: Captures the complex interplay of pedestrian attention and intention.
Applications: Crucial for training models to recognize pedestrian actions, enhance traffic safety, and facilitate the development of advanced driver-assistance systems (ADAS).
Challenges: Addresses the need for fine-grained analysis, such as recognizing subtle cues from pedestrians.
Website: Link to JAAD Dataset
Visionary Co-Driver
Notes: 后置，不是自己研究的时间顺序，而是论文的逻辑实现技术

## Slide 28: JAAD dataset --- the video dataset for pedestrian intention prediction
Visionary Co-Driver
Notes: 后置，不是自己研究的时间顺序，而是论文的逻辑实现技术

## Slide 29: User study
How do we evaluate the system in a Human-Computer Interaction Experiment?
Visionary Co-Driver

## Slide 30
User Study Procedure (by my teammate)
Keywords: 非注意力盲视，分心，认知负荷，SWAT, UEQ
Visionary Co-Driver

## Slide 31: Failure & success
What did I learn from this summer research projects?
Visionary Co-Driver

## Slide 32: Failure Case 1 System Delay
The connected model system is too slow.
Real time consideration is important,
But may be not so important
Solution:
Preprocessing for the ARHUD
Visionary Co-Driver

## Slide 33: Failure Case 2 Pose Estimation
- Intends to include pose direction for more detailed explanation and description.
- Analyzing pose bone is complex and challenging.
- May still need a neural network to determine the direction a person is facing.
Visionary Co-Driver

## Slide 34: Failure Case 3: VQA(Visual Question Answering)
Given a picture and text question(prompt), the model can give appropriate feed back
Natural approach of considering the vision2text task
however, it don’t work for now, too stupid. There is still not practical modal for common sense justification.
Visionary Co-Driver

## Slide 35: Failure Case 3: VQA(Visual Question Answering)
Can’t recognize color the person is wearing
Can’t distinguish left and right
Can’t distinguish young or old
It is too unstable(50% success rate), so we don’t use it
Visionary Co-Driver

## Slide 36: Failure Case 4
- Spent too much time on COT.
- As a big fan of AI agents such as Voyager and code-interpreter, devoted significant time to a major task.
- Possible disparity between personal desire and actual ability.
- Ambitious ideas necessitate a substantial team and extended time periods for success.
Visionary Co-Driver

## Slide 37: Possible IDEA: LLMs as Agent
Intuition: Let GPT itself decide when to function call other api, obtain more information from the current screen.
Because
the VQA performance can be enhanced in Multiple Object scenario.
This sounds like a more ‘human-like’ behavior
Other Agent: Voyager, AutoGPT…
Visionary Co-Driver

## Slide 38: Blind, But Visionary Co-driver
LLMs should actively call APIs, not just passively collect information.
They should probe conditions at upcoming intersections, acting as agents to perform analysis tasks.
This enables automated information collection and data analysis.
Suggested action includes writing an API segment to:
  Extract interesting areas or boxes from an image.
  Generate text from images.
  Use Visual Question Answering (VQA) or call existing APIs to produce additional textual information.
Visionary Co-Driver

## Slide 39: Why is our work more valuable even after visual GPT4 come out?
Vision involves inherent knowledge, and implicit reasoning.
Our approach has higher interpretability and requires less computational power
Prioritizing driving scenarios, breaking down scenes, and detailed descriptions all need further consideration.
Our Success
Visionary Co-Driver

## Slide 40: The End
That’s all, thank you for listening!
Visionary Co-Driver